GLA Format for AIS Aids to Navigation Monitoring Message

INTRODUCTION

One of the functions of the AIS AtoN Transponder is to provide Aids to Navigation monitoring data via AIS message type 6 for the AtoN administration.

This message 6 is an addressed binary message, which is specified by ITU.

MESSAGE INTERVALS

The interval between the transmission of these messages will be synchronized with message 21, although not necessarily at the same reporting rate. If Message 21 is not used at a particular site, then the reporting interval should be selected to minimise the power requirement of the transponder, whilst still providing enough data to enable meaningful diagnostic analysis.

CONFIGURATION

The following fields of the message are fixed, and should be user configurable:

- MMSI number of source Unit

- MMSI number of destination Unit

- Destination Area code (DAC)

- Function Identifier (FI)

| Parameter | Number of bits | Description |
| --- | --- | --- |
| Message ID | 6 | Identifier for this message 6; always 6. |
| Repeat Indicator | 2 | Used by the repeater to indicate how many times a message has been repeated. 0 – 3; default = 0; 3 = do not repeat any more. |
| Source ID | 30 | MMSI number of source Unit |
| Sequence Number | 2 | 0 – 3 |
| Destination ID | 30 | MMSI number of destination Unit. |
| Retransmit Flag | 1 | Retransmit Flag should be set upon retransmission: 0 = no retransmission = default 1 = retransmitted. |
| Spare | 1 | Not used. Should be zero. |
| DAC | 10 | Destination Area Code. Default: 235 (UK & NI) or 250 (ROI) |
| FI | 6 | Function Identifier Default: 10 for this GLA standard message |
| Analogue (internal) | 10 | 0.05– 36V 0.05V step Supply voltage to AIS Unit 0 – Not Used |
| Analogue (external - from hardware analogue input No 1 | 10 | 0.05 – 36V 0.05V step 0 – Not Used |
| Analogue (external - from hardware analogue input No 2 | 10 | 0.05 – 36V 0.05V step 0 – Not Used |
| Status Bits 0 / 1 (internal – same as the 5 LSBs of status bits from Message type 21) | 5 | 4 \ / 00 – no RACON installed; 01 – RACON not monitored 3 / \ 10 – RACON operational; 11 – RACON ERROR 2 \ / 00 – no light or no monitoring; 01 – Light ON 1 / \ 10 – Light OFF; 11 – Light ERROR 0 0 - Good Health, 1 - Alarm |
| Status Bits 0 / 1 (external - derived from hardware digital inputs) | 8 | 7 Digital Input Off/ / On : : 0 Digital Input Off/ / On |
| Off Position Status | 1 | Off position or On position 0: On position 1: Off position |
| Spare | 4 | For future use. Should be zero. |
| TOTAL OF BITS. | 136 | Occupies 1 slot. |